## Slide 1
Gayoung Yang
Intelligence Robotics Lab
School of Intelligent Mechatronics Engineering
Sejong University
2024.12.11
Vision-based Intelligent Gait Environment Detection System for Soft Ankle Exoskeleton
Master Degree Thesis

## Slide 2
Index
I. Introduction
IV. Experiments
VI. Conclusion
II. Soft Exosuit
1. Soft Exosuit Prototype
2. Control Strategy
V. Results
1. YOLO-LSTM based approach
2. EfficientNet-HED based approach
III. Environment Recognition System
1. YOLO-LSTM based approach
2. EfficientNet-HED based approach
Notes: Here is the content of this presentation

## Slide 3
I. Introduction
functional impairments & gait disturbances
foot drop : reduction in foot clearance (swing phase of gait cycle)
- assist gait for stair environment
Lower Limb Exoskeleton
Stroke Patients
common activity
challenging task : joint range, muscular moment ↑
ascent: insufficient clearance between foot & stair nosing
nosing
clearance
stair ambulation

## Slide 4
I. Introduction
inertial measurement unit (IMU) & insole sensor
provide current state of gait
Limitation: Lack of prior environmental information
vision – based perception
visual recognition of step location
continuous monitoring stage
human
peripheral vision
vision system for exoskeleton
awareness of surrounding environment
locomotion guidance
Exoskeleton

## Slide 5
I. Introduction
Deep learning-based methodologies
Vision-based Intelligent gait environment detection algorithm for ankle exosuit
influence robotics field
environment classification + exoskeleton
[challenge]
- transition phase accuracy
- stroke patient consideration
Integration of deep learning-based environment classification into exoskeleton application
detailed gait environment classification (YOLOv8) + spatio-temporal feature extraction (LSTM)
soft ankle exosuit aimed at stroke patients

## Slide 6
II . Soft Exosuit
IMU: gait phase detection
flexible and lightweight materials
Bowden cable-driven method
waist belt
thigh brace
shin brace
curve strap
foot wearable
armour vest
camera: capture
gait environment
flowchart of gait-environment-based exoskeleton control strategy
Exosuit Design
Control Strategy

## Slide 7
III . Environment Recognition System
[customized dataset]
level ground and stair environment
960 x 540 pixel
training: 16,000 | valid: 2,000 | test: 2000
-> 8:1:1
LG
IC
IC prev
IC next
DC
DC prev
DC next
LG
IC
DC
initial incline
final incline
mid-incline
level ground
initial decline
mid-decline
final decline
train
valid
test
Data Acquisition · Class Definition

## Slide 8
III . Environment Recognition System
YOLOv8 Model Training
object detection framework: one-stage detection approach
provide real-time contextual insight for frame
Rapid Detection: critical for detecting gait environment transitions
Spatial analysis: Effective in analyzing global spatial information
input image
frame (i)
YOLOv8
[Hyperparameter]
Epohcs: 100
Batch size: 16
Learning Rate: 0.0001
Optimizer: Adam
[Framework]
Trained using PyTorch on:
Intel i5-13600KF CPU
NVIDIA RTX 3070 GPU
output feature
(8)
feature map
- class probability
- top 1 class
sequential time-series data
consider past and future context
Gait
LSTM
YOLOv8 Environment Classification

## Slide 9
III . Environment Recognition System
YOLOv8
environment classification
output feature
(8)
[class probability, top 1 class]
extract temporal features: adapting to environment transitions
LSTM-Based Spatio-Temporal Feature Extraction
input image
frame (i)
feature sequence
(10,8)
feature
frame (i)
i+10
LSTM1 layer
LSTM
LSTM
LSTM
LSTM
LSTM2 layer
fully connected layer
(128)
class
(3)
softmax
DC
IC
LG
Data Preparation
Frame Sampling: 20 FPS
1 class for 10 frames,
with a stride of 5 (4 labels/sec)
Sequence shape: (1714, 10,8)
Class Labeling
Most probable Class:
Chosen from YOLO frame-wise probabilities
Maximum Voting & Average Voting
Model Training
1000 epochs
batch sizes : 32
learning rate: 0.001
Adam optimizer
LSTM-Based Spatio-Temporal Feature Extraction

## Slide 10
IV . Experiments
Incline
Decline
Level Ground
Experimental Setup
Condition
without exosuit (No Exo)
Exosuit worn but unpowered (Exo Off)
Exosuit worn and powerd (Exo On)
10-minute familarization with exosuit
20-minute rest between conditions
Camera
Surface EMG Sensors:
Medial gastrocnemius
(MG)
Tibialis anterior
(TA)
Inertial sensor
: Xsens MTw Awinda
Exosuit
ankle joint angles (sagittal plane)
Muscle Activation
MVC Normalization
fourth-order Butterworth filter (6Hz cutoff frequency)
gait environment frame

## Slide 11
V . Results
Real-Time Environment Classification Performance
YOLO
Low Recall in Transition Classes ( , )
Overall F1 score : 0.774 - transition misclassification
YOLO - LSTM
Overall F1 score : 0.971 - balanced classification performance
YOLO
Misclassified LG as stairs 1.5s (6 frames) before stair transition
YOLO - LSTM
rapid and accurate classification during the transition phase

## Slide 12
(A)
(B)
(C)
V . Results
Joint Kinematics
peak ankle joint dorsiflexion angle
LG: significant increase with the exo on
IC: increase with the exo on, exo off
6.74° ± 2.08°
25.08° ± 3.63°
25.99° ± 2.78°
27.13° ± 5.71°
25.65° ± 5.16°
21.06° ± 2.08°
exo off
exo on
8.88° ± 3.95°
9.14° ± 2.27°
7.92° ± 1.48°
no exo
LG
IC
DC

## Slide 13
V . Results
(C)
(B)
(A)
Muscle Reduction
average TA muscle activation
LG, IC: reduction in exo off , exo on condition
DC: slight increases with exosuit
12.77% ± 5.02%
12.34% ± 10.93%
15.24% ± 12.77%
13.22% ± 3.43%
12.09% ± 4.81%
9.79% ± 10.12%
exo off
exo on
20.63 ± 11.56%
10.75% ± 4.25%
18.44% ± 9.92%
no exo
LG
IC
DC

## Slide 14
V . Results
Muscle Reduction
(C)
(B)
(A)
average MG muscle activation
LG, IC, DC: reduction in exo on condition
8.51% ± 4.04%
7.62% ± 3.41%
10.66% ± 5.99%
4.87% ± 1.21%
6.41% ± 2.19%
4.70% ± 1.69%
exo off
exo on
7.88% ± 6.61%
9.97% ± 7.35%
11.71% ± 8.83%
no exo
LG
IC
DC

## Slide 15
V . Conclusion
vision-based detection algorithm for an ankle exosuit, focusing on improving gait support for stroke patients
integration of YOLOv8 for environment classification and LSTM for spatio-temporal recognition
rapid and accurate classification during gait environment transition
increased ankle dorsiflexion / Reduced TA and MG muscle activation
Conclusion
Validate across diverse real-world scenarios and multiple stroke patients
Enhance the effectiveness and generalization ability of the exosuit by improving environment classification algorithm
Future work

## Slide 16
Call for Paper
This Special Issue will focus on the latest advances in the field of soft technologies for robot realization. Here, we invite you to share your latest findings by submitting high-quality manuscripts that address the following challenges in the field:
Soft actuators and pliable mechanisms in robotics;
Artificial muscles;
Material and structural design of soft actuators;
Soft materials in soft actuators or robots;
…
Contact us:
Prof. Dr. Brian Byunghyun Kang
brianbkang@sejong.ac.kr
Actuators Editorial Office actuators@mdpi.com
Deadline for manuscript submissions: 31 March 2025
https://www.mdpi.com/journal/actuators/special_issues/L21IU2ZFN9
Special Issue: Recent Advances in Soft Actuators, Robotics and Intelligence

## Slide 17
Intelligence Robotics Lab
School of Intelligent Mechatronics Engineering
Sejong University
Thank You
Gayoung Yang
2024.10.30
Notes: Thank you for your attention, and I welcome any questions or discussions on our research.
질문 답변이 어려운 경우: I don’t have information about this yet